# Introduction

Two-step rotary vane compact vacuum pump is fundamental equipment for vacuuming the sealed container. It can be broadly used to deflate gas for painting machine, medical device, vacuum package, gas analysis and thermoplastic modeling, also be a fore pump if high vacuum degree is needed. It features:

1. Oil reflux proof

The inlet channel is specially designed to prevent the pump oil from flowing back to

the container and channel after ceasing the pump.

2. Environment proof

Isolation layer is put on the oil case as well as air-oil separator on the outlet in order to

obtain no oil spurting and reduce the oil pollution.

3. Alumina alloy shell

For a high efficiency of heat extraction and a durable utility, this equipment adopts

alumina alloy shell.

4.  Stable start-up

This equipment can be stably started due to a large drive moment, either at a low

temperature (≥-5 ºC) in winter or low voltage (≥ 180 V).

5.  Forced-feed lubrication system

This system provide clean and filtered oil which means reduced maintenance and

lower operating cost.

6. Shockproof

Elastomeric coupling is installed between the motor and module to decrease the noises

made by body shock.

# Specification

| Model | 2TW-4C |
| --- | --- |
| Power Supply | 110v/60 Hz or 220v/50 Hz (Optional) |
| Pumping Rate | 13.6 m3/h ( 8.0 CFM, 226 liter / m ) |
| Limited Pressure | 6.7x10-4 mbar |
| Power | 3/4 HP (550W) |
| Max. Rating Speed | 1700 r/min |
| Oiling-Coasting | 450 ml |
| Inlet Fitting | 1/4" SAE (Male) x 1/2" Acme (Male) |
| Oil Inlet Diameter | 9mm |
| Dimension | 400mm x 142mm x 265mm |
| Weight | 22 Kg |
| Certificated | CE Approval |

# Structure

Figure 1

MTI Corporation

860 South 19th Street,

Richmond, CA 94804, USA

TEL: (510)525-3070     FAX: (510)525-4705

Web site:  www.mtixtl.com    E-mail:info@mtixtl.com

# Text boxes

Gas Outlet

Oil Inlet

Handle

Oil-Air Separator

Gas Inlet

Oil Level

Vane Shell

Motor

Oil Tank