MTI Corporation – Graphite MSDS

Address: 860 South 19th Street, Richmond, CA 94804 USA

Phone: 510-525-3070

Fax:  510-525-4705

Email: Sales@mtixtl.com

Product: Carbon / Graphite Grades

| (1) Identification |  |
| --- | --- |
| Chemical Family | Carbon |
| D.O.T. Hazard Classification | Inert |
| (2) Ingredients (Inert and Hazardous) |  |
| Ingredients / Composition | Synthetic Carbon and Graphite C.A.S. # 7782-42-5. Percent PEL 15 mg/M3 TLV 10 mg/M3 >99% |
| (3) Physical Data |  |
| Boiling Point | None |
| Melting Point | None |
| Evaporation Rate | None |
| Solubility in Water | None |
| Appearance | Grey-black solid |
| Volatile by Weight | < 0.01% |
| Specific Gravity | 1..5-2.2 |
| Vapor Pressure | Negligible at room temperature |
| Vapor Density | Negligible at room temperature |
| Odor | None |
| (4) Fire and Explosion Data |  |
| Flash Point | None |
| Lower/Upper Explosive Limit | None |
| Extinguishing Media | Water, CO2, sand |
| Extinguishing media to Avoid | None |
| Hazardous Decomposition Products | In normal combustion, CO2 and CO |
| Special Fire Fighting Procedures | Self-contained breathing apparatus, as normal |
| Unusual Fire and Explosion Data | Graphite and carbon dusts are normally not explosive, but these may weakly contribute if another explosive dust or gas initiates the event. Graphite and carbon dusts are electrically conductive; dust accumulations may cause electrical short circuits or other electrical malfunctions. |
| (5) Health Hazard Data |  |
| Permissible Exposure Limit (PEL) | See Section 2 |
| Primary Routes of Entry | Inhalation of dust. |
| Effects of Overexposure |  |
| Eyes | At high dust level, mechanical irritation. |
| Breathing | Prolonged and repeated overexposure may lead to benign pneumoconiosis. |
| Swallowing or kin | No effect |
| First Aid |  |
| Eyes | Flush with water if irritation occurs and obtain medical assistance. |
| In on Skin, Breathed, or Swallowed | None necessary. |
| Medical Conditions Recognized As Possibly Aggravated By Exposure | Individuals with pre-existing chronic respiratory impairments or with serum antitrypsin deficiency may be at increased risk of pneumoconiosis. |
| (6) Reactivity Data |  |
| Hazardous Polymerization | Will not occur |
| Incompatibility (Materials to Avoid) | None Known |
| (7) Spill or Leak Procedures |  |
| Steps to be Taken in Case Material is Released or Spilled | Use normal housekeeping practice. Vacuum or sweep loose particles or dust. |
| Waste Disposal Method | Bury in an approved landfill. Disposal must be in compliance with Federal, State, & Local laws and regulations. |
| (8) Protective Equipment to be Used |  |
| Respiratory Protection | Use approved respirator if exposure exceeds PEL limits. |
| Ventilation | Local ventilation recommended if dust level exceeds PEL limits |
| Protective Gloves | Not required |
| Eye Protection | If airborne particles are produced wear safety glasses with side shields. |
| Other protective equipment | Not required |
| (9) Special Precautions With comments |  |
| When Machining | Prevent dust escape into atmosphere. Do not breathe dust. |
| (10) References |  |
| ACGIH | Documentation of Threshold Limit Values, current edition |
| NIOSH | Occupational Health Guidelines |
| OSHA | Publication 2006 (29 CFR 1910.1000) |

THIS MATERIAL SAFETY DATA SHEET IS PROVIDED SOLELY FOR YOUR INFORMATION CONSIDERATION AND INVERSTIGATION. ANY USE OF THESE DATA AND INFORMATION MUST BE DETERMINED BY THE USER TO BE IN COMPLIANCE WITH APPLICABLE FEDERAL, STATE, AND LOCAL LAWS AND REGULATIONS.