Material  Safety Data Sheet: Silicon    	                         Page 1of 2

MTI Corporation						Telephone: (510) 525-3070

860 South 19th Street					              Fax: (510) 525-4705

Richmond, CA  94804						www.mtixtl.com

USA

Section 1, Product Identification

Trade Name: Silicon					Synonyms: Elemental Silicon

Chemical Nature: Non-metal				Formula: Si

OSHA PEL: 15 mg/m^3		ACGIH TLV: 10 mg /m^3            Other: 5 mg/m^3 resp

Sec. 302:  No			Sec. 304: No			Sec. 313: No

Section 2: Composition/Ingredients

INGREGIENT				CAS#					Percent

Si						7440-21-3				100

Section 3: Physical/Chemical Data

Boiling Point: 2355 ~ 2600 deg C			Specific Gravity (H2O=1):2.33 gm/cc

Vapor Pressure (mm Hg): 1mm at 1724 deg C	Vapor Density (Air = 1): N/A

% Volatile by Volume: 0				Evaporation Rate (Butyl Acetate=1):  0

Solubility in Water: Insoluble			Melting Point: 1410 ~ 1420 deg C

Appearance and Odor: Steel gray pieces or dark brown powder or substrates, odorless

Section 4: Fire and Explosion Hazard Data

Flash Point: N/A	  Flammable Limits: Nonflammable  LEL: N/A  UEL: N/A; Autoignition Temp: N/A

Extinguishing Media: Flammable solid in powdered form. If involved in fire, don’t use water, Co2, or

halogenated extinguishing agents.  Use dry chemical extinguishing agents, dry sand or dry ground

dolomite.

Special Fire Fighting Procedures: No special firefighting procedures needed.  Use normal procedures

which include wearing NIOSH/MSHA approved self-contained breathing apparatus, flame and

chemical resistant clothing; hats, boots and gloves.  If without risk, remove material from the fire

area.  Cool container with water from maximum distance.  Fumes from fires are hazardous.  Isolate

runoff to prevent environmental pollution.

Fire and Explosion Hazards: Elemental silicon is flammable when exposed to flame or by chemical

reaction with oxidizing agents.  May have a violent reaction with alkali carbonates; oxidants;

(Al+PbO); Ca; CsC2; CaF2; F2; IF3; MnF3; Rb2C2; FNO; AgF; and NaK alloy.  When heated it will

react with water or steam to produce hydrogen gas.

Fire Fighting Equipment: Use NIOSH/MSHA approved self contained breathing apparatus and full

protective clothing if involved in fire.

Section 5: Reactivity Data

Stability: Stable

Incompatibility (Materials to Avoid): Alkali carbonates, (Al+PbO); Ca; CsC2; CaF2; F2; IF3; MnF3;

Rb2C2; FNO; AgF; and NaK alloy.

Conditions to Avoid: None

Hazardous Polymerization: Will not occur   	Hazardous Decomposition Products: Hydrogen gas

Material  Safety Data Sheet: Silicon    	                           Page 2of 2

Section 6: Health Hazard Data

Effects of Exposure:   To the best of our knowledge the chemical, physical and toxicological

properties of silicon have not been thoroughly investigated and recorded.

Routes of Entry (Under Normal Conditions of Use):

Inhalation – No		Skin – No		Ingestion – No		Eye – No

Potential Health Hazards (Acute);  No chronic health effects recorded:

Eyes: dust and powder etc. direct contact may cause abrasive irritation.

Skin: Direct contact may cause abrasive irritation.

Inhalation: May cause abrasive irritating

Ingestion: No acute health effects recorded

Target Organs: No target organs recorded

Medical Conditions: If any, Aggravated by the Chemical: Pre-existing respiratory disorder.

Carcinogenicity:

NTP – Not 		IARC Monograph – No		OSHA Regulated – No

Emergency and First Aid Procedures: Treat symptomatically

Remove From Exposure Immediately.  Contact Physician in all Cases.

Eyes: Flush eyes including under eyelids with copious amounts of water for 15 minutes.  Contact physician immediately.

Skin: Remove contaminated clothing, flood skin with large amounts of water.  If irritation occurs, seek medical attention.  Launder clothing before reuse.

Inhalation: Remove victim to fresh air.  Seek immediate medical attention.

Ingestion: No specific information available.  Contact physician immediately.

Section 7: Precautions for Safe Handling and Use

Steps to be Taken in Case Material is Released or Spilled: Non toxic; treat as ordinary waste

Waste Disposal Method: Non Toxic; Treat as ordinary waste    In accordance with Local, State, and

Federal regulations for the disposal of germanium.  It may be possible to return to supplier for reclaim.

Other Precautions: If broken, material should be treated as with ordinary glass; it is very sharp

Section 8: Control Measures

Respiratory Protection: High efficiency particle respirator if dust is generated.

Ventilation: Local Exhaust recommended.

Protective Gloves: Wear cut-resistant gloves if necessary

Eye Protection: Wear ANSI approved safety glasses if necessary

Other Protective Clothing or Equipment: No special clothing or equipment required under normal

condition of use

Work/Hygienic Practices: No special work/hygienic practices required under normal conditions of

use.   Lab coat and apron.  Always use normal housekeeping and good personal hygiene.

________________________________________________________________________________ MSDS Prepared By: Tony Yang,        Environment, Health & Safety Manager\           4/5/2013