TC100 AG Desk-Top Spin Coater 5100RPM

TC-100 Desk-top Spin Coater is designed for material research lab to make quality sol-gel coating at the lowest cost.  Complete accessories are included for immediate use

Features:

o    Casting aluminum structure case to keep spining stable

o    Two 4" stainless steel spin plates are included , which can hold one or multi samples by wax or double side tape (please click here to lean how to mount sample on the plate  by removable double side tape. It is easy and economic than vacuum chunk))

o    Digital display with variable speed up to 5100 RPM

o    Precision timer can set spinning time from 1- 60 seconds or 1 - 60 minutes (adjustable )

o    Support rod and swing arm of injector are included for easy coating

o    One 100 mL  syringes included for ready coating

o    Flexible water pipe with switch is built in for easy washing

o    One roll of 3M removable double side tape (3/4' W x 400" L ) included for immediate use

o    Input Power:  110V / 240V AC  selectable by and can be used worldwide

o    Dimension:     400mm x 300mm x 200 mm  ( 16”x 12” x  8”)

o    Weight:  20kgs

o  Shipping dimension:18" x 14" x 15"

o  shipping weight:   45  lbs

MTI Corporation

2700 Rydin Road, Unit D, Richmond,  CA 94804, USA

Tel: 510-525-3070     Fax: 510525-4705      E-mail:  info@mtixtl.com       Website:  www.mtixtl.com