Unipol-300 Automatic Mini (3") Grinder/ Polisher for Single Specimen Preparation

Unipol 300 is a semi-auto mini-grinder / polisher for preparing TEM, metallography, and substrate samples in a single mount. The machine equips with many advanced features, such as 3" fix lapping plate, variable sample moving speed, adjustable pressure load and selectable time switch to achieve attention free polishing. Unipol 300 simulates human hand to grind and polish sample via randomly moving sample holder on top versus fixed 3" plate.   It is very suitable for preparing < 1" dia specimen in  low volume laboratory for material research, failure analysis and medical test.  By combining our  SYJ150 low speed saw,  you can own a processing lab on one desk to prepare versatile specimen at affordable budget

Features:

- Easy to use and affordable price.

- Variable moving speed for the sample holder on top

- Adjustable pressure load by a spring inside from 0 - 5 Newtons

- Automatic timer setting from 0 to 99 hours

- One rubber polishing bowl with one 3" glass lapping plates are included

- Extra rubber bowl and 3" glass lapping plate are available as option.

- Two 1" dia. sample holders are included

  - one for flat sample as shown inside plate in the picture left

  - Another holder for inserting bulk sample as shown on top machine.

  - Compressing or cold mount sample can be used as sample holder ( make a hole in round sample mount ceneter, put movong rod on the hole )

- Power:  AC 110V and 220V selectable for worldwide operation.

- Max. moving weight of specimen:  200g

- Max. sample size:  25 mm dia.  x  20 mm H

- Overall dimension: 420mm L x 190mm W x 210mm H.

- Net Weight:  24 lbs

- Package dimension: 18" x 11" x 9"

- Shipping weight: 32 lbs

_____________________________________________________

MTI Corporation

2700 D Rydin Road, Richmond, CA 94804, USA

tel: 510-525-3070  fax: 510-525-4705   Email: sales@mtixtl.com  website: www.mtixtl.com