Unipol 820 Heavy Duty ( 8") Dual Platens Grinding / Polishing Machine with Complete Accessories

UNIPOL-820 is heavy duty  grinding / polishing machine with two 8" lapping plates and independent speed control. This polishing machine is perfect for metallographic lab to prepare small sample faster and easier. Complete accessories are included for immediate use, including two diamond lapping plate, polishing pad and diamond paste etc.

Features :

- Heavy duty fiberglass case with anti corrosion painting surface

- Power:         110V or 220 V  switchable power supply, worldwide support

- Motor:          Two  300W high torque DC motor with belt pulley with independent speed control

- Variable speed:             from 0 - 600 RPM with digital display for each plate

- Two 8" Aluminum lapping plates can be quickly released and installed.

- Soft rubber splah cover for safe operation

- Dimension:                    580 L x 420 W X 350 H (mm)

- Aprox. net weight:          44 Kg

- Complete accessories included for immedate use ( > $100 value )

  - Two 8" Aluminum lapping plates, which can be quickly released and installed.

  - Two  PSA diamond lapping plates for faster gringing ( 320 mesh and 600 mesh )

  - Two Black polishing pad for final polisging

  - 10g diamond polishing paste ( 0.5 micron grit ) for final polishing

- Total shipping weight accessories:  60 kg

- Shipping package dimension:    650 mm x 550 mm x 450 mm  in  Paper board box

MTI Corporation

2700 Rydin Road, Unit D, Richmond,  CA 94804, USA

Tel: 510-525-3070     Fax: 510525-4705      E-mail:  info@mtixtl.com       Website:  www.mtixtl.com