24 T Desktop Hydraulic Pressing Machine

with Built in Manual Pump & Protection Cover

Model YLJ-24T is a desktop dry pressing machine up to 24 metric tons for materials / chemistry research laboratories to prepare compound ceramic sample. YLJ-24T has built in hydraulic pump with auto return function and transparent protection shield.

Main Specifications:

| Max.pressure | 24 metric tons |
| --- | --- |
| Pump | hand pump built inside frame |
| Bottom hydraulic cylinder travel distance | 20 mm |
| Top support screw adjustable height | 150 mm |
| Working space under frame | 105 (L) x 105(W) x 150 (H), mm |
| Dimension of machine | 270 (L) נ200 (W) נ450 (H), mm |
| Net weight | 34 Kg ( 75 lbs) |
| Dimension of shipment | 14" x 14" x 25" |
| Weight of shipment | 100 lbs |

MTI Corporation  --- Leading mfg for advanced materials & Lab equipment since 1995

2700 Rydin Road, Unit D, Richmond,  CA 94804, USA

Tel: 510-525-3070     Fax: 510525-4705      E-mail:  info@mtixtl.com       Website:  www.mtixtl.com