40T Desktop Electric Hydraulic Pressing Machine

Model YLJ-40TA is electric hydraulic pressing machine up to 40 metric tons for preparing compound or ceramic sample faster and easy. YLJ-40TA has built in hydraulic pump which is driven by electric oil pump with larger pressure gauge. It is an excellent tool for material / ceramic / chemistry laboratories to make larger pellet sample.

Main Specifications:

| Max. Pressure | 40 Metric Tons |
| --- | --- |
| Pressure stability | 1MPa /10min |
| Electric hydraulic pump | Standard: 220V AC ( single phase ) 180W Optional: 110V-220V transformer for using under 110V |
| Bottom hydraulic cylinder travel distance | 0 - 25 mm |
| Top support scew adjustable height | 180 mm |
| Working space under frame | 155 (L) x 100(W) x 180 (H), mm |
| Dimension of Machine | 370 (L) x 350 (W) x 450 (H), mm |
| Net Weight | 55 Kg ( 121 lbs) |
| Dimension of shipment | 18" x 18" x 25" |

MTI Corporation  --- Leading mfg for advanced materials & Lab equipment since 1995

860 South 19th Street, Richmond,  CA 94804, USA

Tel: 510-525-3070     Fax: 510525-4705      E-mail:  info@mtixtl.com       Website:  www.mtixtl.com