Material  Safety Data Sheet:         Strontium Titanate		  Page 1of 3

MTI Corporation					Telephone: (510) 525-3070

2700 Rydin Road, Unit D				Fax: (510) 525-4705

Richmond, CA  94804					www.mtixtl.com

USA

Section 1, Product Identification

Trade Name: Strontium Titanate				Synonyms: N/A

Chemical Nature: Metal Oxide				Formula: SrTiO3

OSHA PEL: N/E					ACGIH TLV: N/E

Section 2: Composition/Ingredients

INGREGIENT				CAS#					Percent

Strontium Titanate			 1206-05-9				100

Section 3: Physical/Chemical Data

Boiling Point: Not established				Specific Gravity (H2O=1): No data

Vapor Pressure (mm Hg): No Data 			Vapor Density (Air = 1): >1

% Volatile by Volume: 0					Evaporation Rate (Butyl Acetate=1):  0

Solubility in Water:  Insoluble				Melting Point: Approx 2060 deg C

Solubility in Mineral Acids: N/A

Appearance and Odor: White-gray odorless solid

Section 4: Fire and Explosion Hazard Data

Flash Point:  None  					Auto-ignition Temp: N/A

Flammable Limits: Upper: N/AF				Flammable Limits in Air, by Volume: N/A

Extinguishing Media: Non-combustible.  If involved in a fire use dry ground Dolomite, dry sand, or powdered Graphite.  DO NOT USE WATER

Special Fire Fighting Procedures: If involved in a fire wear NIOSH/MSHA approved self-contained breathing apparatus, flame and chemical resistant protective clothing hat, gloves and boots to prevent contact with skin and eyes.  If without risk move material out of fire area

Unusual Fire and Explosion Hazards: may emit toxic fumes if involved in a fire

Section 5: Reactivity Data

Stability: Stable				Conditions to Avoid: Not applicable

Incompatibility (Conditions to Avoid): Strong Acids and bases

Hazardous Polymerization: Will not occur

Hazardous Decomposition Products: May emit toxic fumes when heated to decomposition (strontium oxide, titanium oxide).

Section 6: Health Hazard Data

Routes of Entry :

Inhalation – Yes		Skin – Yes		Ingestion – Yes		Eye – Yes

Threshold Limit Value: Not established

Medical Conditions Generally Aggravated by Exposure:  Pre-existing respiratory disorders.

Carcinogenicity:  None listed

NTP – Not Listed		IARC Monograph – No		OSHA Regulated – No

Target Organs: No target organs for strontium titanate have been recorded.

Material  Safety Data Sheet:		Strontium Titanate    	 Page 2 of 3

Health Hazards (Acute and Chronic):

To the best of our knowledge the chemical, physical and toxicological properties of strontium titanate have not been thoroughly investigated and recorded.

Strontium compounds have a low order of toxicity.  It is chemically and biologically similar to calcium.  The oxides and hydroxides are moderately caustic materials.  For titanium compounds, these materials are considered to be physiologically inert.  There are no reported cases in the literature where titanium as such has caused intoxication.  The dusts of titanium compounds such as titanium oxide may be placed in the nuisance category. (Sax, Dangerous Properties of Industrial Materials, sixth edition)

Inhalation:

Acute: May be a nuisance dust.  May cause coughing and shortness of breath

Chronic: No chronic health effects recorded.

Ingestion:

Acute: No acute health effects recorded

Chronic: No chronic health effects recorded.

Skin:

Acute: May cause irritation.

Chronic: No chronic health effects recorded

Eyes:

Acute: May cause irritation.

Chronic: No chronic health effects recorded

Signs and Symptoms of Overexposure:

Inhalation: May cause sneezing, coughing and dry throat.

Ingestion: No acute or chronic health effects recorded.

Skin: May cause redness, itching.

Eyes: May cause redness, itching and watering.

Emergency and First Aid Procedures: Treat symptomatically

Eyes: Flush eyes with lukewarm water for 15 minutes.  Seek medical attention.

Skin: Remove contaminated clothing.  Brush material off skin and exposed area.  Wash affected area with soap and water.  Seek medical attention.

Inhalation: Remove victim to fresh air, keep warm and quiet,  Administer oxygen if breathing is difficult.  Seek medical attention

Ingestion: Give 1-2 glasses of milk or water and induce vomiting.  Seek immediate medical attention.

Section 7: Precautions for Safe Handling and Use

Steps to be Taken in Case Material is Released or Spilled: Wear a self-contained breathing apparatus and full protective clothing.  Stop leak if without risk, cover spill with soda ash.  Collect into a properly marked container and submit or retain for disposal or salvage.

Waste Disposal Method: In accordance with Local, State and Federal Waste Disposal Regulations.

Material  Safety Data Sheet:	Strontium Titanate    		Page 3 of 3

Section 8: Control Measures

Respiratory Protection (Specify Type): Wear NIOSH-approved dust mask for ordinary use and self-contained breathing apparatus for emergency use.

Ventilation: Local Exhaust: Maintain concentration at low exposure levels

Mechanical:  Recommended

Protective Gloves: Neoprene; Rubber 			Eye Protection: Safety Glasses

Other Protective Clothing or Equipment: Laboratory coat and apron.  Eye wash fountain capable of sustained flushing.  Safety drench shower, hygienic facilities for washing.

Other Handling and Storage Conditions:

- Wash thoroughly after handling

- Keep container tightly closed

- Use adequate ventilation

- Store away from acids.

Precautionary Labeling: WARNING!   IRRITANT!  DO NOT INHALE DUST!  EYE CONTACT MAY CAUSE IRRITATION!

The above information is accurate to the best of our knowledge.  However, since data, safety standards, and government regulations are subject to change, and the conditions of handling and use or misuse are beyond our control, ESPI makes no warranty, either expressed or implied, with respect to the completeness or continuing accuracy of the information contained herein, and disclaims all liability for reliance thereon. Users should satisfy themselves that they have all current data relevant to their particular application.

MSDS Prepared By: Tony Yang,     Environment, Health & Safety Manager\   Date: January   /2007