# 12" Precision Auto Lapping/Polishing Machine - EQ-Unipol-1202

# with Two 4" Work Stations

UNIPOL-1202 machine is equipped with 12" super flat lapping plate and can be used as a high precision lapping machine for polishing crystal components, semiconductor wafers, and ceramic substrates up to 4" in diameter. It can be used as a standard grinding and polishing machine for preparing metallographic samples as well.

SPECIFICATIONS

| Super-Flat 12" (300 mm) Diameter Lapping Plate | Flatness < 0.25 micron / inch² |
| --- | --- |
| Precision Rotating Shaft | Running Off < 5 micron |
| Heavy Duty Cast Aluminum Case with Bright Painting | Color : Black or White |
| Features | One cast iron plate for lapping and one cast aluminum plate for polishing. Two rocking work stations with wafer holders and condition rings, which can be controlled independently for polishing 2 pcs of 4" wafers at the same time. |
| Two Work Stations with 8° Rocking and adjustable speed | 9 rocking / minute |
| Two Flat Sample Holders for Carrying < 4" Dia. Wafer | 105 Dia. x 35 T mm |
| Two Condition Rings | 120 O.D. x 110 I.D. x 32 T mm |
| Variable Speed of Master Plate with Digital Display | 0 ~ 150 rpm |
| Adjustable Timer for Auto-Stop | 0 - 99 hours |
| Power | 120V or 240 V selectable via switch |
| Motor | 300 W high torque DC motor |
| Dimensions | 700 L x 475 W x 300 H (mm) |
| Weight | 154 lbs |
| Dimensions of shipment | 43" x 31" x 33" |
| Weight of shipment | 200 Lbs |
| Optional Parts | SKZD-2 Automatic Slurry Feeder 2" Polishing Fixture for Precision / Automatic Thinning and Polishing Polishing Sample Holder with Three 1" Holes for Metallurgraphy |
| Compliance | CE Certified |
| Warranty | One year limited with lifetime support Rusting and damage due to improper storage condition or maintenance is not covered by warranty |

MTI Corporation

860 South 19th Street, Richmond, CA 94804, USA

Tel: 510-525-3070     Fax: 510525-4705      E-mail:  info@mtixtl.com       Website:  www.mtixtl.com